## Slide 1
Source: US EPA National Stormwater Calculator Release 1.1.0.0
- reduced peak rates for all design storms up to 100-year, 24-hour (reductions range from 18-27%), especially for smaller, more frequent storm events
- no net increase in stormwater runoff volume for up to the 2-year, 24-hour storm (stream channel protection)
- provides treatment of and virtual elimination (via infiltration and evapotranspiration) of “first flush” runoff event (i.e. 1” storm); accounts for approximately 85-90% of annual storm events (typically)
- promotion of infiltration and groundwater recharge; mimics existing hydrology
- less disturbance/grading, especially on west side of Elm Place
- enhanced water quality compared to conventional design
- habitat creation (vegetated infiltration features)
- opportunity for public education and technology demonstration
- enhances site aesthetics / quality of life / property values
LID
Baseline

## Slide 2
Pollutant | Total Est. Pollutant Reduction (lb/yr)
Total Suspended Solids (TSS) | 8,599
Total Phosphorus (TP) | 50
Total Nitrogen (TN) | 391
88% reduction in pollutant loading over conventional design due to filtration of first 1” (first flush) of rainfall in swales, rain gardens and other bioretention areas. Reduction based on pollutant load calculator developed for Wichita, KS.
Peak rate and volume calculations using the SCS method of calculation
Chart: Stormwater Run-off Volume Comparison for Commercial Development
| 1 year | 5 year | 10 year | 25 year | 50 year | 100 year
Conventional | 3.94 | 5.02 | 6.9 | 8.47 | 11.32 | 12.74
LID | 1.4 | 2.11 | 3.9 | 5.37 | 8.08 | 9.59
Chart: Stormwater Run-off Peak Rate Comparison of Residential Area
| 1-year | 2-year | 5-year | 10-year | 50-year | 100-year
Existing | 18.94 | 30.29 | 52.33 | 72.2 | 109.97 | 129.6
Conventional | 25.79 | 36.59 | 50.22 | 67.71 | 73.54 | 79.52
LID | 12.92 | 20.83 | 39.27 | 55.23 | 84.13 | 97.96
24% to 58% volume reduction

## Slide 3: Costs
Residential
  11,300 lf underground conveyance
  98 inlets
  Zero porous pavement
  Zero biorentation area
  30,000 cy of mass grading plus 8,000 cy of fill
  108,000 sf of retention ponds
  Curbs throughout residential neighborhood
$5,800,000
LID
  2,822 lf underground conveyance
  30 inlets
  29,549 sf porous pavement
  114,797 sf bioretention areas
  Minimal mass grading (layouts follow natural slope of existing site)
  18,000 sf retention ponds incorporated into natural drainage
  No curbs
$5,500,000